## Slide 1: Spectrum Deconvolution
Determination Of Different Radionuclides in a Mixture
Eric Einspänner

## Slide 2: Spectrum deconvolution
  = count rate in each channel i
  = number of radionuclides ( = Lu, = Iod)
  = unknown true count rate of nuclid n
  = content of the corresponding channel i of the pure (reference) spectrum of nuclid n
is the normalised spectrum of n ()
m channels -> m equations
Spectrum deconvolution:
  Def.: The shape of a measured sample spectrum is used for resolving its components by fitting the pure (reference) spectrum of
  each component to the measured composite spectrum.
Mathematically:
  least-square fitting method (optimizing)
  find by minimizing the sum of the squared differences (measured) and (predicted) rates for all channels

## Slide 3
no smoothing
Optimizer = Nelder-Mead
Spectrum:
  Lu-177m: 99.5Bq
  Lu-177: 39.2 Bq
  Iod: 92.8 Bq
Calculated:
  Iod: 119.5 Bq
  Lu: 140.4 Bq ( 47.6 Bq → 51.3%)
    Smoothing?

## Slide 4
Savitzky-Golay filter for smoothing
Optimizer = Nelder-Mead
1. Mixture:
Real:
  Lu-177m: 99.5Bq
  Lu-177: 39.2 Bq
  Iod: 92.8 Bq
Calculated:
  Lu-177m : 106.7 Bq
  Iod: 103.3 Bq ( 10.5 Bq →11.31%)
2. Mixture:
Real:
  Lu-177m: 96.4 Bq
  Lu-177: 37.8
  Iod: 46.2 Bq
Calculated:
  Lu-177m : 101.8 Bq
  Iod: 55.6 Bq ( 9.4 Bq →20.35%)
3. Mixture:
Real:
  Lu-177m: 86.2 Bq
  Lu-177: 33.6 Bq
  Iod: 4.6 Bq
Calculated:
  Lu-177m : 98.7 Bq
  Iod: 4.6 Bq (0 Bq →0%)

## Slide 5: How good is Spectrum deconvolution?
Advantages
only one measurement necessary for activity determination
additional nuclides can be added
General: easy adaptation to similar use cases
results can be further improved, if necessary, by adjusting the parameters
fast and smart ;)
Disadvantages
various factors have an influence on the result
  data quality
  smoothing filter
  optimizer
  …
results only with smoothing filter with small errors
co-existence of Lu-177m and Lu-177 not considered.